## Slide 1: InterVLAN

## Slide 4: Configure Inter-VLAN Routing
configure inter-VLAN routing

## Slide 5: Configure Inter-VLAN Routing
the steps to configure inter-VLAN routing

## Slide 6: Inter VLAN
S1 (S2#, S3#) # conf t
  S1# ip default-gateway 172.17.99.1
  S1# ip http server
VTP
  #vtp mode server
  #vtp domain test
  #vtp password cisco

## Slide 7: Inter VLAN
port 할당
  # int range fa0/1-5
  #sw mode trunk
  #sw trunk native vlan 99
  # int range fa0/6-10
  #sw mode access vlan 30
VLAN 생성
  #vlan 99
  #name management
관리 인터페이스 주소 할당
  #int vlan 99
  #ip add 172.17.99.11 255.255.255.0
  #no shutdown

## Slide 8: Inter VLAN
Router
  # int fa0/1
  #no sh
  #int fa 0/1.1
  #encap dot1q 1
  #ip add 172.17.1.1 255.255.255.0
  #int fa0/1.10
  #encap dot1q 10
  #ip add 172.17.10.1 255.255.255.0
  #int fa0/1.99
  #encap dot1q 99 native
  #ip add 172.17.99.1 255.255.255.0

## Slide 9: Summary
Router on a stick
  this is an inter-VLAN routing topology that uses router sub interfaces connected to a layer 2 switch.
  Each Subinterface must be configured with:
  An IP address
  Associated VLAN number
Configuration of inter VLAN routing
  Configure switch ports connected to router with correct VLAN
  Configure each router subinterface with the correct IP address & VLAN ID
Verify configuration on switch and router