## Slide 1: VLAN

## Slide 2
vlan 생성 1
  (config) vlan 10
  (config- vlan)# name ENG
vlan 생성 2
  vlan database
    vlan10
    vlan 10 name ENG
vlan port 설정
access port
  Interface fa0/0 (int range fa0/1-10)
  switchport mode access
  switchport mode access vlan 10
trunk port
  interface fa0/5
  switchport mode trunk
  switchport trunk encapsulation dot1q
  switchport trunk allowed vlan 10
  switchport trunk vlan add 10
  switchport trunk vlan add 20
show interface switchport fa0/5
show interface trunk

## Slide 3
vlan IP 할당
  interface vlan 10
    ip address 192.168.10.2 255.255.255.0
    ip default-gateway 192.168.10.1 255.255.255.0
inter vlan
  R1> int fa0/0
    no sh
    int fa0/0.10
    encapsulation dot1q 10
    ip address 192.168.10.1 255.255.255.0

## Slide 4
Native VLAN : dot1q 트렁크 포트가 Untagged 프레임을 수신하면 처리하는 VLAN(기본값 VLAN 1) - Untagged 프레임 : dot1q Tag 정보(VLAN-ID)가 없는 이더넷 프레임

## Slide 5
VTP Pruning
  config)#vtp pruning
  int fa0/1
    sw tr pruning vlan 2-10
    sw tr pruning vl all
    sw tr pruning vlan add 2-10
    sw tr pruning vlan remove 2-10
    sw tr pruning vlan except 2-10